## Slide 1
DUT : SWITCH CORE
FCS and control
MAC Learner
Crossbar
tx_data[31:0]
tx_ctrl[3:0]
reset
link_sync
rx_data[31:0]
rx_ctrl[3:0]
w_datafifo_full = 0
length_fifo_full = 0
status_fifo_full = 0
dstmac_fifo_full = 0
srcmac_fifo_full = 0
len_full = 0 (per scheduler)
fifo_full = 0
no write when full
no read when empty
occupancy warnings
ASSERTIONS
TX Monitor
Observes tx_data/tx_ctrl
Reconstructs frames per output port
Decodes MAC addresses
Counts frames
Outputs:
Actual frames per port
SWITCH DRIVER
Computes expected behavior
Maintains MAC learning model
Splits frames to expected destination ports
Drives frames onto RX interface
Outputs:
RX stimulus
Expected frames per port
SCOREBOARD
Matches actual frames with expected frames (per port)
Compares full frame contents (byte by byte)
Reports mismatches and unexpected frames
Maintains error count and total comparisons
FINAL REPORT
PASS/FAIL (Errors, comparisons)
Actual Frame Mailboxes (act_q[3:0])
One mailbox per output port
Expected Frame Mailboxes (exp_q[3:0])
One mailbox per output port
TEST SCENARIOS
TC1-TC10